## Slide 1: Air Pollution Analysis

## Slide 2: Project analysis slide 2
Air Pollution
Dataset Analysis
EDA
ANALYSIS
DASHBOARD
CONCLUSION
Agenda

## Slide 3: Project analysis slide 3
Pollutant
RSPM
SO2
NO2
PM2.5
SPM
Respirable Suspended Particulate Matter - particulate matter with diameter of less than or equal to 10 micrometres. They are produced from combustion process, vehicles and industrial sources
Sulphur Dioxed
Nitrogen Dioxed
Particles with an aerodynamic diameter less than 2.5μm
Suspended Particulate Matter - such as dust, fumes, mist, and smoke. The concentration of these in and near the urban areas causes severe pollution to the surroundings

## Slide 4
EDA
Getting The Data
Analysing the Data
  Data Information
  Data description
  Checking Duplicates Values
  Checking Missing Values
  Checking Unique Values
Data Filteration & Modification
  Dropping unnessesary column and replacing the texts in “type”
  Handling Null Values
Air Quality Index

## Slide 5
 | stn_code | sampling_date | state | location | agency | type | so2 | no2 | rspm | spm | location_monitoring_station | pm2_5 | date
0 | 150.0 | February - M021990 | Andhra Pradesh | Hyderabad | NaN | Residential, Rural and other Areas | 4.8 | 17.4 | NaN | NaN | NaN | NaN | 1990-02-01
1 | 151.0 | February - M021990 | Andhra Pradesh | Hyderabad | NaN | Industrial Area | 3.1 | 7.0 | NaN | NaN | NaN | NaN | 1990-02-01
2 | 152.0 | February - M021990 | Andhra Pradesh | Hyderabad | NaN | Residential, Rural and other Areas | 6.2 | 28.5 | NaN | NaN | NaN | NaN | 1990-02-01
3 | 150.0 | March - M031990 | Andhra Pradesh | Hyderabad | NaN | Residential, Rural and other Areas | 6.3 | 14.7 | NaN | NaN | NaN | NaN | 1990-03-01
4 | 151.0 | March - M031990 | Andhra Pradesh | Hyderabad | NaN | Industrial Area | 4.7 | 7.5 | NaN | NaN | NaN | NaN | 1990-03-01
1. Getting The Data

## Slide 6
2. Analysing the Data
i. Data Information :
<class 'pandas.core.frame.DataFrame'>
RangeIndex: 435742 entries, 0 to 435741
Data columns (total 13 columns):
# Column Non-Null Count Dtype
--- ------ -------------- -----
0 stn_code 291665 non-null object
1 sampling_date 435739 non-null object
2 state 435742 non-null object
3 location 435739 non-null object
4 agency 286261 non-null object
5 type 430349 non-null object
6 so2 401096 non-null float64
7 no2 419509 non-null float64
8 rspm 395520 non-null float64
9 spm 198355 non-null float64
10 location_monitoring_station 408251 non-null object
11 pm2_5 9314 non-null float64
12 date 435735 non-null object
dtypes: float64(5), object(8)
memory usage: 43.2+ MB
None

## Slide 7
ii. Data description :
 | so2 | no2 | rspm | spm | pm2_5
count | 401096.000000 | 419509.000000 | 395520.000000 | 198355.000000 | 9314.000000
mean | 10.829414 | 25.809623 | 108.832784 | 220.783480 | 40.791467
std | 11.177187 | 18.503086 | 74.872430 | 151.395457 | 30.832525
min | 0.000000 | 0.000000 | 0.000000 | 0.000000 | 3.000000
25% | 5.000000 | 14.000000 | 56.000000 | 111.000000 | 24.000000
50% | 8.000000 | 22.000000 | 90.000000 | 187.000000 | 32.000000
75% | 13.700000 | 32.200000 | 142.000000 | 296.000000 | 46.000000
max | 909.000000 | 876.000000 | 6307.033333 | 3380.000000 | 504.000000

## Slide 8
iii. Checking Missing Values :
Data columns with null values : | 
stn_code | 144077
sampling_date | 3
state | 0
location | 3
agency | 149466
type | 5357
so2 | 34632
no2 | 16222
rspm | 40035
spm | 236908
location_monitoring_station | 27303
pm2_5 | 425754
date | 7

## Slide 9
v. Checking Unique Values :
Data columns with unique values : | 
stn_code | 803
sampling_date | 5485
state | 37
location | 304
agency | 64
type | 10
so2 | 4197
no2 | 6864
rspm | 6065
spm | 6668
location_monitoring_station | 991
pm2_5 | 433
date | 5067

## Slide 10
i. Dropping unnessesary column and replacing the texts in “type”:
3. Data Filteration & Modification
stn_code, agency & sampling_date this two features is irrelevant to our analysis so let's remove this feature
We are replacing it all the types of locations and getting them down to only 4 following categories:
    Residential Area
    Industrial Area
    Sensitive Area
    RIRUO

## Slide 11
 | state | location | type | so2 | no2 | rspm | spm | location_monitoring_station | pm2_5 | date
0 | Andhra Pradesh | Hyderabad | Residential Area | 4.8 | 17.4 | NaN | NaN | NaN | NaN | 1990-02-01
1 | Andhra Pradesh | Hyderabad | Industrial Area | 3.1 | 7.0 | NaN | NaN | NaN | NaN | 1990-02-01
2 | Andhra Pradesh | Hyderabad | Residential Area | 6.2 | 28.5 | NaN | NaN | NaN | NaN | 1990-02-01
3 | Andhra Pradesh | Hyderabad | Residential Area | 6.3 | 14.7 | NaN | NaN | NaN | NaN | 1990-03-01
4 | Andhra Pradesh | Hyderabad | Industrial Area | 4.7 | 7.5 | NaN | NaN | NaN | NaN | 1990-03-01
OUTPUT :

## Slide 12
ii. Handling Null Values :
As we have seen already that in some features the null values are very few so we can remove those rows directly, it will hadrly effect our overall analysis. Below are the features that we are removing:
  location
  Date
And also we have seen that there few feature columns having a huge chunk on missing values. By dropping those rows from tha dataset will negetively effect our further analysis, so instead of removing those null values we are going to replace them with the "mean value". Below are the features that we are going to replace values:
  so2
  no2
  rspm
  spm
  pm2_5

## Slide 13
OUTPUT :
 | state | location | type | so2 | no2 | rspm | spm | location_monitoring_station | pm2_5 | date
0 | Andhra Pradesh | Hyderabad | Residential Area | 4.8 | 17.4 | 108.833091 | 220.78348 | NaN | 40.791467 | 1990-02-01
1 | Andhra Pradesh | Hyderabad | Industrial Area | 3.1 | 7.0 | 108.833091 | 220.78348 | NaN | 40.791467 | 1990-02-01
2 | Andhra Pradesh | Hyderabad | Residential Area | 6.2 | 28.5 | 108.833091 | 220.78348 | NaN | 40.791467 | 1990-02-01
3 | Andhra Pradesh | Hyderabad | Residential Area | 6.3 | 14.7 | 108.833091 | 220.78348 | NaN | 40.791467 | 1990-03-01
4 | Andhra Pradesh | Hyderabad | Industrial Area | 4.7 | 7.5 | 108.833091 | 220.78348 | NaN | 40.791467 | 1990-03-01

## Slide 14
4. Air Quality Index
AQI: The air quality index is an index for reporting air quality on a daily basis. In other words, it is a measure of how air pollution affects one’s health within a short time period. The AQI is calculated based on the average concentration of a particular pollutant measured over a standard time interval. Generally, the time interval is 24 hours for most pollutants, 8 hours for carbon monoxide and ozone.
We can see how air pollution is by looking at the AQI level:
  Good(0 – 50)
  Moderate(51 – 100)
  Unhealthy(101 – 150)
  Unhealthy for Strong People(151 – 200)
  Hazardous(201+)

## Slide 15
 | so2 | Si
0 | 4.8 | 6.000
1 | 3.1 | 3.875
2 | 6.2 | 7.750
3 | 6.3 | 7.875
4 | 4.7 | 5.875
 | no2 | ni
0 | 17.4 | 21.750
1 | 7.0 | 8.750
2 | 28.5 | 35.625
3 | 14.7 | 18.375
4 | 7.5 | 9.375
Sub indexe of NO2 : As per the Indian Government, safe exposure is 0-80 ug/m3 (24 hours) and as per US-EPA, it is 0-53 ppb (1 hour).
If the value lies between 0 – 40 then we will “NO2*(50/40)” or the value lies between 41 – 80 then we wil “50+(NO2-14)*(50/40)” and so on.
Sub indexe of SO2 : The safe exposure level is 0-80 ug/m3 (24 hours) and 0-75 ppb (1 hour) according to the Indian government
If the value lies between 0 – 40 then we will “SO2*(50/40)” or the value lies between 41 – 80 then we wil “50+(SO2-40)*(50/40)” and so on.
Sub indexes :
Indian AQI | Indian Range for SO2 (ug/m3)
0-50 | 0-40
51-100 | 41-80
101-200 | 81-380
201-300 | 381-800
301-400 | 801-1600
401-500 | 1600+
Indian AQI | Indian Range for NO2 (ug/m3)(24 hours)
0-50 | 0-40
51-100 | 41-80
101-200 | 81-180
201-300 | 181-280
301-400 | 281-400
401-500 | 400+
Output :
Output :

## Slide 16
 | rspm | rpi
435734 | 148.0 | 122.666667
435735 | 131.0 | 117.000000
435736 | 140.0 | 120.000000
435737 | 143.0 | 121.000000
435738 | 171.0 | 130.333333
 | spm | spi
435734 | 220.78348 | 180.52232
435735 | 220.78348 | 180.52232
435736 | 220.78348 | 180.52232
435737 | 220.78348 | 180.52232
435738 | 220.78348 | 180.52232
Output :
Output :
Sub indexe of rspm : If the value lies between 0 – 30 then “rspm*(50/30)” or the value lies between 30 – 60 then “50+(rspm-30)*(50/30)” or the value is between 60-90 then 100+(rspm-60)*(100/30) and so on. If the value is more than 250 then “400+(rspm-250)*(100/130)”
Sub indexe of spm : If the value lies between 0 – 100 then we will “we will use the same present in the dataset” or the value lies between 100 – 250 then “100+(spm-100)*(100/150)” or the value lies between 250 – 350 then “200+(spm-250)” or the values between 350 – 450 then “300+(spm-350)*(100/80)“. If the value is more than 450 then “400+(spm-430)*(100/80)”

## Slide 17
 | date | state | si | ni | rpi | spi | AQI
0 | 1990-02-01 | Andhra Pradesh | 6.000 | 21.750 | 109.61103 | 180.52232 | 180.52232
1 | 1990-02-01 | Andhra Pradesh | 3.875 | 8.750 | 109.61103 | 180.52232 | 180.52232
2 | 1990-02-01 | Andhra Pradesh | 7.750 | 35.625 | 109.61103 | 180.52232 | 180.52232
3 | 1990-03-01 | Andhra Pradesh | 7.875 | 18.375 | 109.61103 | 180.52232 | 180.52232
4 | 1990-03-01 | Andhra Pradesh | 5.875 | 9.375 | 109.61103 | 180.52232 | 180.52232
Output :

## Slide 18: Project analysis slide 5
Nitrogen Dioxed
24.85
Average Of NO2
Sulphur Dioxed
.
9.97
Average Of SO2
Suspended Particulate Matter
100.50
Average Of spm
Analysis
Respirable Suspended Particulate Matter
98.79
Average Of rspm
Air Quality Index
188.58
Average Of AQI

## Slide 19
Chart: Average Of SO2 by Year
| 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Total | 21.8271 | 22.0981 | 18.6681 | 17.7231 | 17.6077 | 17.7198 | 21.9589 | 22.4789 | 26.0009 | 20.6456 | 21.28 | 20.0318 | 20.289 | 16.9139 | 15.2507 | 13.1518 | 6.5571 | 11.5343 | 12.8293 | 11.3084 | 11.6549 | 11.2699 | 10.7308 | 10.0896 | 11.2013 | 10.8978 | 9.2499 | 9.1375 | 8.4059
Chart: Top 10 Polluted States
| Bihar | Delhi | Jharkhand | Maharashtra | Punjab | Rajasthan | Uttar Pradesh | Uttarakhand | Uttaranchal | West Bengal
Average of no2 | 36.5755 | 53.4891 | 43.3663 | 32.1154 | 28.0858 | 30.441 | 27.6101 | 26.9381 | 27.163 | 59.0757
Average of rspm | 123.7052 | 196.6398 | 168.5178 | 101.4796 | 173.4937 | 142.0168 | 176.9523 | 148.9789 | 121.6943 | 115.0399
At 1995 the value of so2 is 26.00 and at 2003 the value of so2 is 6.55
West Bengal as no2 value as 59.07 and Delhi as no2 value as 53.48 it also has rpsm value as 196.63 and the Maharashtra as rspm value as 101.47

## Slide 20
Chart: Pollutants Distribution By Type
| Industrial Area | RIRUO | Sensitive Area | Residential Area
Average of so2 | 13.4113 | 10.9126 | 6.1186 | 9.5196
Average of no2 | 29.4628 | 31.7799 | 19.9594 | 24.0399
Average of spm | 241.367 | #N/A | 235.1391 | 208.5656
Average of rspm | 122.0484 | 103.6173 | 99.5227 | 102.4329
Chart: Pollutants Distribution By Type
| Industrial Area | RIRUO | Sensitive Area | Residential Area
Average of so2 | 13.4113 | 10.9126 | 6.1186 | 9.5196
Average of no2 | 29.4628 | 31.7799 | 19.9594 | 24.0399

## Slide 21
Dashboard

## Slide 22
Conclusion
As we can see that at West Bengal, Delhi, Haryana & Rajasthan high AQI values and at the industrial area the air pollution is high compared to other types (considering all the types). While comparing between SO2 & NO2, NO2 is high in both industrial area and RIRUO.
Key influencers :
NO2 :– In state “West Bengal, Delhi, Jharkhand, Maharashtra, Rajasthan” , In types the industrial area and the top segment is West Bengal having average value of 58.68 it’s more the overall average 24.85.
SO2 :– In state “Jharkhand, Maharashtra, Gujarat” , In types the industrial area and the top segment is Maharashtra having average value of 16.77 it’s more the overall average 9.97

## Slide 23: Thank You